## Slide 1: Use Cases and Requirements for QUIC as a Substrate
Mirja Kühlewind
IETF-105 ER MASQUE side meeting
2019-07-25

## Slide 2: Goal
Use QUIC a substrate/tunnelling protocol to proxies/VPN server/load balancers…
  Utilize QUIC's ability to multiplex, encrypt data, and migrate between network paths
Make network support functions collaborative and explicit
  Client and/or server selects proxy and function
  Tunnelling and encryption protects information exchanged with a proxy from other network interference

## Slide 3: Approach
Client explicitly opens QUIC tunnel connection to proxy
  use of HTTP CONNECT and MASQUE for forwarding, authentication, and configuration
QUIC proxy provides secure forwarding and performance enhancement services
  e.g. congestion control support (mobile/satellite), access policy enforcement, load balancing/mobility, multi-hop chaining/onion routing
QUIC proxy may optionally also open a tunnel to server (if supported by server)

## Slide 4: Connection Establishment
QUIC CHELLOouter A
QUIC SHELLOouter A
CONNECTouter A (Server) + QUIC CHELLOinner
QUIC packetinner
QUIC packet
QUIC packet
OKouter A + QUIC SHELLOinner
Outer QUIC tunnel
QUIC CHELLO
QUIC SHELLO
Client
(QUIC)
Proxy
Server (QUIC)
QUIC packetinner+ ACKouter A
Inner QUIC connection

## Slide 5: Usage Scenarios draft-kuehlewind-quic-substrate
Obfuscation via Tunnelling
  Client knows proxy and connects to request forwarding
    Client and proxy have a trust relationship and can optionally authenticate each other (see MASQUE)
  Server is not aware of the proxy and does not see the clients IP address
Advanced Support of User Agents
  Proxy provides additional functionality (located "close" to the client e.g. access network)
  Clients request function and may provide information to the proxy; optionally server can be aware
  Security and Access Policy Enforcement
Frontend Support for Load Balancing and Migration/Mobility
  (Reverse) proxy may or may not be under the the same administrative domain as the service provider
  Proxy supports load balancing and/or mobility without terminating the e2e/app security association
  IoT Gateways
Multi-hop Chaining (aka Onion Routing)

## Slide 6: Requirements and Open Issues
Trust and authentication
Control protocol and support functions
Discovery

## Slide 7: Drafts
QUIC as a Substrate - https://tools.ietf.org/html/draft-kuehlewind-quic-substrate-00
MASQUE - https://tools.ietf.org/html/draft-schinazi-masque
HTTP Transport Authentication - https://tools.ietf.org/html/draft-schinazi-httpbis-transport-auth-00
Also, previous and related drafts:
  HELLIUM - https://tools.ietf.org/html/draft-schwartz-httpbis-helium
  HINT - https://tools.ietf.org/html/draft-pardue-httpbis-http-network-tunnelling
  QUIC Datagram - https://tools.ietf.org/html/draft-pauly-quic-datagram